## Slide 1: MR-PET
Mirjam Lenz, Uwe Pietrzyk
Institute of Neurosciences and Medicine (INM) Research Center Juelich, Germany
A new module for the EduGATE Project
part one: particle sources
Department of Mathematics and Natural Sciences University of Wuppertal, Germany
Contact: u.pietrzyk@fz-juelich.de or uwe.pietrzyk@uni-wuppertal.de
Basic Paper „Zeitschrift für Medizinische Physik“ (Z. Med. Phys. 23 (2013) 65-70)
1

## Slide 2
Long is the way of theory,
short and effective by examples –
(Lucius Annaeus Seneca (the Younger),
Epistulae morales)

## Slide 3: MR-PET
Introduces to the basic physical effects in MR-PET hybrid imaging
Provides with GATE-macros
Provides programme code for ROOT to visualize basic behaviour of charged particles
in the magnetic field of a MR System

## Slide 4: general setup of the MR-PET module
source emits charged particles or photons of defined energy
particles interact with surounding medium (impact ionisation, compton scattering,...)
annihilation of positrons can be enabled (by default disabled)
additional deviation due to magnetic field (B0)
detection of particles in surrounding medium

## Slide 5: exemplary setup of the MR-PET module
electrons (80 keV) are emitted isotropically from a point source (positioned at the origin)
electrons interact with the medium(air), annihilation turned off
trajectories of electrons are plotted as red lines
no additional magnetic field

## Slide 6: exemplary setup of the MR-PET module
electrons (80 keV) are emitted from an isotropic source (positioned at the origin)
electrons interact with the medium (air), annihilation turned off
trajectories of electrons are plotted as red lines
magnetic field in z direction: B0 = 0.5 T

## Slide 7: orientation of the coordinate system
point-like
source at center
(x = y = z = 0)
X
Z
Y

## Slide 8: particle sources
choose from three different particle sources: electron, positron or gamma*) source
specify the type of particle propagation (isotropic or beam source)
*) use the gamma source to investigate effects of secondary electrons

## Slide 9: particle sources
beam direction: +y
isotropic

## Slide 10: shapes of surounding medium
cube
particles interact immediately within medium
cylinder
initial deviation due to magnetic field visible (if enabled), followed by interaction within medium

## Slide 11: Please note:
Within GATE ‚crystal‘ denomiates the volume in which particles are detected
it does not have to be a crystal (like a scintillator) but consists of air, water or lung tissue, etc.
to prevent misunderstanding the ‘crystal’ is called ‚medium‘ in this macro

## Slide 12: user interface (Gate_v7.0 or 7.1)
type „./config_starter_mac_70.csh“ in a terminal window
specify parameters like source energy, source activity, medium etc.
choose point of view if visualisation is enabled
generate configuration and start simulation

## Slide 13: user interface (Gate_v7.0 or 7.1)
take a look at the scene under different angles by changing (ϑ,ϕ)
X
Z
Y
ϑ
ϕ

## Slide 14: user interface (Gate_v7.0 or 7.1)
selection presets can be modified in „MR_PET.txt“
Visualisation: disabled; enabled;
ViewPointThetaPhi: 0 90; 30 30; 90 0; -90 0; 89 90; 15 30; 30 30; 45 45; 60 60;
particle: e-; e+; gamma;
Annihilation: disabled; enabled;
SourceEnergy: 10; 30; 50; 80; 90; 100; 120; 140; 160; 200; 240; 400; 600; 800; 1000; 1600;
SourceActivity: 100; 1000; 10000; 100000;
Camera_Type: cube; cylinder;
Source_Type: beam_x; beam_y; beam_z; iso;
Medium: Air; Water; Lung; Liver;
B0_x: 0.0; 0.1; 0.2; 0.3; 0.4; 0.5; 1.0; 3.0; 7.0; 9.4; 12.0; 15.0; 20.0;
B0_y: 0.0; 0.1; 0.2; 0.3; 0.4; 0.5; 1.0; 3.0; 7.0; 9.4; 12.0; 15.0; 20.0;
B0_z: 0.0; 0.1; 0.2; 0.3; 0.4; 0.5; 1.0; 3.0; 7.0; 9.4; 12.0; 15.0; 20.0;

## Slide 15: user interface (Gate_v7.0 or 7.1)
use „MR_PET.C“ to evaluate a specific .root file (file browser opens automatically after simulation)
further information in terminal window
[Acquisition-0] ============= Acquisition starts! =============
[Acquisition-0] Simulation start time = 0 sec
[Acquisition-0] Simulation end time = 100 sec
[Acquisition-0] Simulation will have = 10 run(s)
…
##### Reading from file: MR_PET_cube_Water_800_e-_10_beam_x_0.0_0.4_0.0_enabled
…
##### Number of emitted particles : 990
##### Number of detected events : 990
##### ratio detected/emitted : 100 %

## Slide 16: analysis with „MR_PET.C“

## Slide 17
no magnetic field

## Slide 18
magnetic field in x direction

## Slide 19
magnetic field in z direction

## Slide 20
magnetic field in y direction

## Slide 21
electron source in lung tissue

## Slide 22
magnetic field in z direction

## Slide 23
magnetic field in z direction

## Slide 24
positron source in water

## Slide 25
magnetic field in z direction

## Slide 26
magnetic field in z direction

## Slide 27
magnetic field in z direction

## Slide 28
Error: illegal pointer to class object hi_energy 0x0 157 MR_PET.C:172
The leaves of the branch you are investigating seem to have no content. Check your simulation settings: can particles be stopped within the medium or can they leave the medium without being detected?
Example: electron source (100 keV) within a cylindrical medium (Air), magnetic field in z direction (0.3 T). The electrons can‘t even enter the medium due to deviation caused by presence of magentic field.
troubleshooting