## Slide 1: MR-PET
Mirjam Lenz, Uwe Pietrzyk
Institute of Neurosciences and Medicine (INM) Research Center Juelich, Germany
A new module for the EduGATE Project
part two: ion sources
2
Department of Mathematics and Natural Sciences University of Wuppertal, Germany
Contact: u.pietrzyk@fz-juelich.de or uwe.pietrzyk@uni-wuppertal.de
Basic Paper „Zeitschrift für Medizinische Physik“ (Z. Med. Phys. 23 (2013) 65-70)

## Slide 2
Long is the way of theory,
short and effective by examples –
(Lucius Annaeus Seneca (the Younger),
Epistulae morales)

## Slide 3: MR-PET
Introduces to the basic physical effects in MR-PET hybrid imaging
Provides with GATE-macros
Provides programme code for ROOT to visualize basic behaviour of charged particles
in the magnetic field of a MR System

## Slide 4
ion source emits charged particles or photons
particles interact with surounding medium (impact ionisation, compton scattering, annihilation of positrons with electrons...)
additional deviation due to magnetic field (B0)
detection of particles in surrounding medium
general setup of the MR-PET module

## Slide 5: orientation of the coordinate system
point-like
source at center
(x = y = z = 0)
X
Z
Y

## Slide 6: shapes of surounding medium
cube
particles interact immediately within medium
cylinder
initial deviation due to magnetic field visible (if enabled), followed by interaction within medium

## Slide 7: Please note:
Within GATE ‚crystal‘ denomiates the volume in which particles are detected
it does not have to be a crystal (like a scintillator) but consists of air, water or lung tissue, etc.
to prevent misunderstanding the ‘crystal’ is called ‚medium‘ in this macro

## Slide 8
type „./config_starter_mac_70.csh“ in a terminal window
specify parameters like source type, source activity, medium etc.
choose point of view if visualisation is enabled
generate configuration and start simulation
user interface (Gate_v7.0 or 7.1)

## Slide 9: user interface (Gate_v7.0 or 7.1)
take a look at the scene under different angles by changing (ϑ,ϕ)
X
Z
Y
ϑ
ϕ

## Slide 10: user interface (Gate_v7.0 or 7.1)
selection presets can be modified in „MR_PET.txt“
Visualisation: disabled; enabled;
ViewPointThetaPhi: 0 90; 30 30; 90 0; -90 0; 89 90; 15 30; 30 30; 45 45; 60 60;
Source_Type: O15; C11; F18; Mn52; I124;
Annihilation: disabled; enabled;
SourceActivity: 10; 50; 100; 500; 1000; 10000; 20000; 100000;
Camera_Type: cube; cylinder;
Medium: Air; Water; Lung; Liver; Vacuum;
B0_x: 0.0; 0.1; 0.2; 0.3; 0.4; 0.5; 1.0; 3.0; 7.0; 9.4; 12.0; 15.0; 20.0;
B0_y: 0.0; 0.1; 0.2; 0.3; 0.4; 0.5; 1.0; 3.0; 7.0; 9.4; 12.0; 15.0; 20.0;
B0_z: 0.0; 0.1; 0.2; 0.3; 0.4; 0.5; 1.0; 3.0; 7.0; 9.4; 12.0; 15.0; 20.0;

## Slide 11: user interface (Gate_v7.0 or 7.1)
use „MR_PET.C“ to evaluate a specific .root file (file browser opens automatically after simulation)
further information in terminal window
[Acquisition-0] ============= Acquisition starts! =============
[Acquisition-0] Simulation start time = 0 sec
[Acquisition-0] Simulation end time = 100 sec
[Acquisition-0] Simulation will have = 10 run(s)
…
##### Reading from file: MR_PET_cube_Water_100_O15_0.0_0.4_0.0_enabled.root
…
##### Number of emitted particles : 10034
##### Number of detected events : 10020
##### ratio detected/emitted : 99.8605 %

## Slide 12
example: 52Mn source in water

## Slide 13
Error: illegal pointer to class object hi_energy 0x0 157 MR_PET.C:172
The leaves of the branch you are investigating seem to have no content. Check your simulation settings: can particles be stopped within the medium or can they leave the medium without being detected?
Example: electron source (100 keV) within a cylindrical medium (Air), magnetic field in z direction (0.3 T). The electrons can‘t even enter the medium due to deviation caused by presence of magentic field.
troubleshooting