## Slide 1: Spectrometry_Gamma A New Module For The EduGATE Project
Uwe Pietrzyk & Michaela Gaens
Institute of Neurosciences and Medicine (INM), Research Center Juelich, Germany
Department of Mathematics and Natural Sciences, University of Wuppertal, Germany
Contact: u.pietrzyk@fz-juelich.de or uwe.pietrzyk@uni-wuppertal.de
(Basic Paper  „Zeitschrift für Medizinische Physik“ / Z. Med. Phys. 23 (2013) 65-70)
Notes: <number>

## Slide 2
Long is the way of theory,
short and effective by examples –
(Lucius Annaeus Seneca (the Younger),
Epistulae morales)
Notes: <number>

## Slide 3
  Spectrometry_Gamma:
    introduces to the basics of gamma spectra obtained from a scintillation detector
    Inspired by chapter 10 of Physics in Nuclear Medicine (Cherry, Sorensen & Phelps, 2012)
    provides GATE-macros
    comes in two versions: Basic & Extended
    Programme Code in C and for ROOT to calculate and plot relevant parameters during Compton Scatter
Notes: <number>

## Slide 4
Pulse-height spectrum for 137Cs showing
typical structures
from: Cherry et al, 2012
Notes: <number>

## Slide 5
Basics of
Compton_Scatter
Esc = E0 /[1 + ( E0 /0.511) (1 − cos)]
Ere = E0 − Esc
for 180-degree scattering:
Escmin = E0 /[1 + (2 E0 /0.511)]
Eremax = E0 – Escmin
(Esc)
(E0)
(Ere)
    (Cherry, et al, 2012)
Notes: <number>

## Slide 6
Code
for (int i=0; i<n_values; i++)
{
// energy of the incident gamma
E_gamma[i] = (i+1) * e_step;
// energy of the recoil electron; -> "compton electron" -> "compton edge"
Emax_re[i] = E_gamma[i] * E_gamma[i] / (E_gamma[i] + m_electron_2);
// energy of the back-scattered gamma
Emin_sc[i] = E_gamma[i] - Emax_re[i];
printf( " E_gamma: %f Emax_re: %f Emin_sc: %f (MeV) \n", E_gamma[i], Emax_re[i], Emin_sc[i]);
}
--> output
E_gamma: 0.010000 Emax_re: 0.000377 Emin_sc: 0.009623 (MeV)
E_gamma: 0.020000 Emax_re: 0.001452 Emin_sc: 0.018548 (MeV)
E_gamma: 0.030000 Emax_re: 0.003152 Emin_sc: 0.026848 (MeV)
E_gamma: 0.040000 Emax_re: 0.005415 Emin_sc: 0.034585 (MeV)
.
.
E_gamma: 0.660000 Emax_re: 0.475806 Emin_sc: 0.184194 (MeV)
E_gamma: 0.670000 Emax_re: 0.485035 Emin_sc: 0.184965 (MeV)
E_gamma: 0.680000 Emax_re: 0.494281 Emin_sc: 0.185719 (MeV)
E_gamma: 0.690000 Emax_re: 0.503543 Emin_sc: 0.186457 (MeV)
E_gamma: 0.700000 Emax_re: 0.512820 Emin_sc: 0.187180 (MeV)
running: root -l compton_scatter_root.c
Notes: <number>

## Slide 7
Plot created via: root -l compton_scatter_root.c
Notes: <number>

## Slide 8
situation for
E = 660KeV
like for 137Cs
Notes: <number>

## Slide 9
Pulse-height spectrum for 137Cs showing
typical structures
full
energy
peak
recoil
electron
gamma,
scattered
at ~180 ° from
surrounding
material
from: Cherry et al, 2012
Notes: <number>

## Slide 10
Spectrometry_Gamma_Basic
head 1
head 0
Notes: <number>

## Slide 11
Basic Setup
simplified Gamma Camera  2 crystals, no collimator,
collimated gamma source
head 1
head 0
Two opposing NaI-crystals allow to detect:
  back-scattered gamma
  characteristic X-ray, escaping from the crystal (head 0)
simplified Gamma Camera  2 crystals, no collimator,
collimated gamma source (rays directed towards head 0 !!)
Notes: <number>

## Slide 12
situation for
E = 511KeV
E_gamma: 0.510000 Emax_re: 0.339778 Emin_sc: 0.170222 (MeV)
Notes: <number>

## Slide 13
511 keV
head 0
head 1
full
energy
peak
recoil electron 
compton edge
gamma, scattered at ~180 °
from head 0 
back-scatter peak
note: different scales!!
Notes: <number>

## Slide 14
Pulse-height spectrum for 197Hg

some more details!!
from: Cherry et al, 2012
Notes: <number>

## Slide 15
80 keV
head 0
head 1
note: different scales!!
Iodine
escape
peak
escape peak: E0 – EX-rays
E_gamma: 0.080 Emax_re: 0.019076 Emin_sc: 0.060924 (MeV)
Iodine (in NaI-crystal):
characteristic X-rays following
photoelectric
absorption
gamma, scattered at ~180 °
from head 0 
back-scatter peak
Notes: <number>

## Slide 16
head 1
E_gamma: 0.080 Emax_re: 0.019076 Emin_sc: 0.060924 (MeV)
Iodine
characteristic
x-rays
http://xdb.lbl.gov/Section1/Periodic_Table/I_Web_data.htm
gamma, scattered at ~180 °
from head 0 
back-scatter peak
Notes: <number>

## Slide 17
Starting Basic Setup (Gate_v7.0)
specify:
energy &
energy resolution
in a shell-window type:
config_starter_mac_70.sh
Notes: <number>

## Slide 18
Starting Basic Setup (Gate_v7.0)
can change selection presets in Spectrometry_Gamma.txt
CameraType: 2heads; 1head; 4heads;
ViewPointThetaPhi: 0 90; 90 0; -90 0; 89 90; 15 30; 30 30; 45 45; 60 60;
VisuOnOff: novisu; visu;
SourceActivity: 100 Bq; 1000. Bq; 10000. Bq; 100000. Bq;
CrystalMaterial: NaI; BGO; LSO; GSO; PWO; LuAP; YAP; CZT; Silicon; Lead; Tungsten;
SourceVolMaterial: Vacuum; Water; Plexiglass; Air; PVC;
SourceType: gamma_collim; gamma;
SourceEnergy: 80; 10; 50; 60; 90; 100; 120; 140; 160; 200; 240; 364; 511; 1000; 1600;
E_res: 0.10; 0.00; 0.01; 0.05; 0.15; 0.20; 0.25;
Notes: <number>

## Slide 19
Result: Basic Setup (Gate_v7.0)
Notes: <number>